## Slide 1
Chemical amendments for the treatment of various types of agricultural effluent
M.G. Healy*, O. Fenton, G. Lanigan, J. Grant, R.B. Brennan, C.J. O’ Flynn, A. Serrenho
ICEPR, Toronto, Ontario, Canada, July 15-17, 2013

## Slide 2
Background
The land area of Ireland is 6.9 m ha, of which 4.6 m ha is used for agriculture.*
Almost 80% of agricultural area is devoted to pasture, hay and grass silage, 11% to rough grazing, and 10% to crop production.*
* Fact sheet on agriculture – April 2012 http://www.agriculture.gov.ie/media/migration/publications/2012/FactsheetonIrishAgricultureApr12.pdf

## Slide 3
Background
In 2010, there were 110,998 farms with cattle
* Census of Agriculture 2010 – Preliminary Results http://www.cso.ie/en/media/csoie/releasespublications/documents/agriculture/2010/coapre2010.pdf

## Slide 4
Background
In 2010, there were 1,214 farms with pigs
* Census of Agriculture 2010 – Preliminary Results http://www.cso.ie/en/media/csoie/releasespublications/documents/agriculture/2010/coapre2010.pdf

## Slide 5
Background
Characterisation of wastewater
Parameter | units | Pig slurry1 | Dairy cattle slurry2 | Dairy soiled water (DSW)3
Total Phosphorus | mg L-1 | 613±40 | 1140±76 | 14.2±0.5
Total Nitrogen | mg L-1 | 2800±212 | 4430±271 | 730±212
Ammonium-N | mg L-1 | 2290 ±39 | 1760 ±123 | 110±35
pH |  | 7.85 ± 0.03 | 7.47 ± 0.05 | 7.9±0.0
Dry matter | % | 3.41± 0.08 | 10.5± 0.04 | 0.2±0.1
1 O’ Flynn C.J., Fenton O., Wilson P., Healy M.G. (2012) J Environ Manage 113, 78 – 84.
2 Brennan R.B., Fenton O., Grant J., Healy M.G. (2011) Sci Tot Environ 409, 5111-5118.
3 Serrenho A., Fenton O., Murphy P.N.C., Grant J., Healy M.G. (2012) Sci Tot Environ 430, 1-7.
Water from concreted areas, hard stand areas and holding areas for livestock

## Slide 6
Background
Currently, land application is the most common method for the disposal of slurries and DSW
Land application of dairy and pig slurry, and DSW can result increased loss of phosphorus (P) to runoff
Slurry application can result in a build-up in soil test phosphorus (STP) increasing chronic P loss

## Slide 7
  Incidental P losses
    Occur when a rainfall event occurs shortly after slurry application and before fertiliser infiltrates the soil
P
P
P
P
P
P
P
P
P
P
P
P
P
P
Slurry P
Soil P
P
P
Background

## Slide 8
  Chronic P losses
    Long-term loss of P from soil as a result of a build-up in STP caused by application of inorganic fertilisers and manure
P
P
P
P
P
P
P
P
P
P
P
Slurry P
Soil P
P
Background

## Slide 9
Background
Critical Source Area (CSA) for P loss
High P source
High transport
potential

## Slide 10
Background
Critical Source Area

## Slide 11
Background
Food Harvest 2020* aims to (by 2020):
  ‘increase the value of primary output in the agriculture and fisheries sector by €1.5 billion.
  Increase value-added output by €3 billion
  Achieve an export target of €12 billion’.
http://www.agriculture.gov.ie/media/migration/agri-foodindustry/foodharvest2020/2020FoodHarvestEng240810.pdf

## Slide 12
Background
Cattle farms Pig farms
This will lead to increased intensification of farming and, in turn, increased loading of nutrients, which may be a threat to water quality.
The land surrounding intensive farmed areas will become P rich
Farmers may have no choice but to use it for landspreading
This could be potentially problematic if the land is located in a CSA

## Slide 13
Objectives
If farmers have no choice but to spread wastewater in high soil test phosphorus areas, which may be located in a CSA, they may be able to add chemical amendments to wastewater to reduce surface runoff.
The aim of this study was to identify suitable chemical amendments for addition to three types of wastewater
dairy cattle slurry
pig slurry and
DSW
to reduce surface runoff of nutrients and suspended sediment (SS) in surface runoff.

## Slide 14
Methodology
Identification of amendments
Determine how much amendments to use per unit volume of wastewater
Efficacy of amendments at laboratory-scale
Efficacy of amendments at field plot-scale
Efficacy of amendments at field-scale
Batch-scale tests
Laboratory-scale tests
Plot and field-scale tests

## Slide 15
Methodology
Batch-scale tests
Laboratory-scale tests
Plot and field-scale tests
Other issues to consider in determination of best amendment:
Potential greenhouse gas emissions
Subsurface leaching of nutrients
Impact on chronic (long-term) losses of nutrients
Identification of amendments
Determine how much amendments to use per unit volume of wastewater
Efficacy of amendments at laboratory-scale
Efficacy of amendments at field plot-scale
Efficacy of amendments at field-scale

## Slide 16
Methodology
Batch-scale tests
Aims:
Identify the most effective amendments to reduce the solubility of P in the wastewater
Identify optimum application rates
Select amendments most suitable for further examination (some may work well, but may cost too much)
‘Stoichometric Tests’
Amount expressed as ratio of weight of amendment to weight of TP
Wastewater

## Slide 17
Chart: kg of amendment added per kg of dry matter
| 0 | 0.85714285714285765 | 1.7142857142857186 | 3.428571428571439 | 5.1428571428571415 | 6.8571428571428363
Flyash | 22.973 | 8.7777 | 4.4467 | 3.0863 | 3.889 | 3.0123
FGD | 22.973 | 15.1953 | 11.262 | 7.5497 | 6.238 | 5.514
Bottom ash | 22.973 | 21.246 | 20.45 | 19.1777 | 18.979 | 17.4093
Gypsum | 22.973 | 17.9637 | 18.213 | 16.0823 | 16.3193 | 13.9387
Al-WTR-1 | 22.973 | 25.8213 | 26.0827 | 26.0433
Al-WTR-2 | 22.973 | 24.2917 | 23.4093 | 22.795 | 21.549 | 19.5957

## Slide 18
Methodology
Batch-scale tests
Aims:
Identify the most effective amendments to reduce the solubility of P in the wastewater
Identify optimum application rates
Select amendments most suitable for further examination (some may work well, but may cost too much)

## Slide 20
Chart: Time from start of agitator test (hours)
| 0.25 | 0.5 | 1 | 2 | 4 | 8 | 12 | 24 | 30
 | 0.67667 | 0.77167 | 0.89567 | 1.1403 | 1.9567 | 1.5837 | 1.614 | 1.53 | 1.5263
 | 133.0361 | 164.2251 | 205.1805 | 281.5074 | 366.8577 | 437.7282 | 479.448 | 499.3418 | 498.6412

## Slide 21
Chart: Time from start of agitator test (hours)
| 0.25 | 0.5 | 1 | 2 | 4 | 8 | 12 | 24 | 30
 | 3.9552 | 5.0118 | 6.1334 | 7.9634 | 10.3708 | 13.963 | 15.4272 | 17.0332 | 17.5695
 | 0.67667 | 0.77167 | 0.89567 | 1.1403 | 1.9567 | 1.5837 | 1.614 | 1.53 | 1.5263
 | 133.0361 | 164.2251 | 205.1805 | 281.5074 | 366.8577 | 437.7282 | 479.448 | 499.3418 | 498.6412

## Slide 22
Chart: Time from start of agitator test (hours)
| 0.25 | 0.5 | 1 | 2 | 4 | 8 | 12 | 24 | 30
5 mL/kg | 2.0887 | 2.5783 | 3.2213 | 4.4197 | 5.7597 | 6.8723 | 7.5273 | 7.8397 | 7.8287
 | 3.9552 | 5.0118 | 6.1334 | 7.9634 | 10.3708 | 13.963 | 15.4272 | 17.0332 | 17.5695
 | 0.67667 | 0.77167 | 0.89567 | 1.1403 | 1.9567 | 1.5837 | 1.614 | 1.53 | 1.5263
 | 133.0361 | 164.2251 | 205.1805 | 281.5074 | 366.8577 | 437.7282 | 479.448 | 499.3418 | 498.6412

## Slide 23
Chart: Time from start of agitator test (hours)
| 0.25 | 0.5 | 1 | 2 | 4 | 8 | 12 | 24 | 30
10 mL/kg | 1.8108 | 2.1288 | 2.5912 | 3.3525 | 4.2985 | 5.3965 | 5.85 | 6.3733 | 5.2325
5 mL/kg | 2.0887 | 2.5783 | 3.2213 | 4.4197 | 5.7597 | 6.8723 | 7.5273 | 7.8397 | 7.8287
 | 3.9552 | 5.0118 | 6.1334 | 7.9634 | 10.3708 | 13.963 | 15.4272 | 17.0332 | 17.5695
 | 0.67667 | 0.77167 | 0.89567 | 1.1403 | 1.9567 | 1.5837 | 1.614 | 1.53 | 1.5263
 | 133.0361 | 164.2251 | 205.1805 | 281.5074 | 366.8577 | 437.7282 | 479.448 | 499.3418 | 498.6412

## Slide 24
Chart: Time from start of agitator test (hours)
| 0.25 | 0.5 | 1 | 2 | 4 | 8 | 12 | 24 | 30
10 mL/kg | 1.8108 | 2.1288 | 2.5912 | 3.3525 | 4.2985 | 5.3965 | 5.85 | 6.3733 | 5.2325
15mL/kg | 1.0813 | 1.2583 | 1.5033 | 2.0023 | 1.804 | 2.4773 | 2.5197 | 2.4573 | 2.4243
5 mL/kg | 2.0887 | 2.5783 | 3.2213 | 4.4197 | 5.7597 | 6.8723 | 7.5273 | 7.8397 | 7.8287
 | 3.9552 | 5.0118 | 6.1334 | 7.9634 | 10.3708 | 13.963 | 15.4272 | 17.0332 | 17.5695
 | 0.67667 | 0.77167 | 0.89567 | 1.1403 | 1.9567 | 1.5837 | 1.614 | 1.53 | 1.5263
 | 133.0361 | 164.2251 | 205.1805 | 281.5074 | 366.8577 | 437.7282 | 479.448 | 499.3418 | 498.6412

## Slide 25
Methodology
Batch-scale tests
Aims:
Identify the most effective amendments to reduce the solubility of P in the wastewater
Identify optimum application rates
Select amendments most suitable for further examination (some may work well, but may cost too much)

## Slide 26
Chart: Total cost of chemical amendment of slurry (euro t-1)
| 6.671148342767296 | 7.1456164968553475 | 12.407899660377362
AlCl2 (PAC) | 12.8809 | 13.6703 | 14.6635
FeCl2 | 13.0252 | 13.3563 | 14.5786
Ca(OH)2 | 0.48808 | 11.056 | 12.0788
Al-WTR-2 | 0.37348 | 10.691 | 10.0331
FGD | 6.6718 | 10.8904 | 12.1637
Flyash | 10.7759 | 13.2417 | 13.6873
Al2(SO4) | 83 | 94 | 99

## Slide 27
Chart: Total cost of chemical amendment of slurry (euro t-1)
| 6.671148342767296 | 7.1456164968553475 | 12.407899660377362
AlCl2 (PAC) | 12.8809 | 13.6703 | 14.6635
FeCl2 | 13.0252 | 13.3563 | 14.5786
Ca(OH)2 | 0.48808 | 11.056 | 12.0788
Al-WTR-2 | 0.37348 | 10.691 | 10.0331
FGD | 6.6718 | 10.8904 | 12.1637
Flyash | 10.7759 | 13.2417 | 13.6873
Al2(SO4) | 83 | 94 | 99

## Slide 28
Results
Batch-scale tests
Most effective amendments identified by the batch-scale tests
Pig slurry1 | Dairy cattle slurry2 | Dairy soiled water3
Alum |  | 
Poly-aluminium chloride |  | 
Ferric chloride (FeCl3) |  | 
Lime |  | 
1 O’ Flynn, C.J., Fenton, O., Healy, M.G. (2012) CLEAN – Soil, Air, Water 40: 164-170.
2 Brennan, R.B., Fenton, O., Rodgers, M., Healy, M.G. (2011) Soil Use Manage 27: 238-246.
3 Fenton, O., Serrenho, A., Healy, M.G. (2011) Water, Air Soil Poll 222: 185-194.

## Slide 29
Results
Batch-scale tests
Most effective amendments identified by the batch-scale tests
Pig slurry1 | Dairy cattle slurry2 | Dairy soiled water3
Alum | Alum | 
Poly-aluminium chloride | Poly-aluminium chloride | 
Ferric chloride (FeCl3) | Ferric chloride (FeCl3) | 
Lime | Lime | 
 | Aluminium-based sludge | 
 | Flue-gas desulfurization by-product (FGD) | 
1 O’ Flynn, C.J., Fenton, O., Healy, M.G. (2012) CLEAN – Soil, Air, Water 40: 164-170.
2 Brennan, R.B., Fenton, O., Rodgers, M., Healy, M.G. (2011) Soil Use Manage 27: 238-246.
3 Fenton, O., Serrenho, A., Healy, M.G. (2011) Water, Air Soil Poll 222: 185-194.

## Slide 30
Results
Batch-scale tests
Most effective amendments identified by the batch-scale tests
Pig slurry1 | Dairy cattle slurry2 | Dairy soiled water3
Alum | Alum | Alum
Poly-aluminium chloride | Poly-aluminium chloride | 
Ferric chloride (FeCl3) | Ferric chloride (FeCl3) | Ferric chloride (FeCl3)
Lime | Lime | Lime
 | Aluminium-based sludge | Bottom ash
 | Flue-gas desulfurization by-product (FGD) | 
1 O’ Flynn, C.J., Fenton, O., Healy, M.G. (2012) CLEAN – Soil, Air, Water 40: 164-170.
2 Brennan, R.B., Fenton, O., Rodgers, M., Healy, M.G. (2011) Soil Use Manage 27: 238-246.
3 Fenton, O., Serrenho, A., Healy, M.G. (2011) Water, Air Soil Poll 222: 185-194.

## Slide 31
Methodology
Identification of amendments
Determine how much amendments to use per unit volume of wastewater
Efficacy of amendments at laboratory-scale
Efficacy of amendments at field plot-scale
Efficacy of amendments at field-scale
Batch-scale tests
Laboratory-scale tests
Plot and field-scale tests

## Slide 32: Laboratory-scale runoff study
Runoff-box experiment designed to examine effectiveness of chemical amendments, identified at bench-scale, under more ‘realistic’ conditions
Examined incidental losses of DRP, suspended sediment (SS), particulate phosphorus (PP) and total phosphorus (TP)
Examined incidental loss of metals (Al, Ca and Fe) to runoff

## Slide 33: Laboratory-scale study
t= -24 hr Pack runoff boxes, then saturate and allow to drain and reach approx. field capacity
t=0 hr Apply slurry
Rainfall simulation:
Intensity 11.5 ± 1mm hr-1
Three 30-min rainfall simulations conducted on each runoff box
t=48 hr RS 1
t=72 hr RS 2
t=96 hr RS 3
24 hr interval
24 hr interval

## Slide 34
1 m
0.225 m
AMENDED
SLURRY
SLOPED RUNOFF BOXES
GRASS SOD
Notes: 34
SOIL FLUME SLURRY AMENDMENT RAINFALL SLOPE RUNOFF

## Slide 35
O’ Flynn et al. 2012. J Env Man 113: 78-84.
Chart: Phosphorus
| 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3
DRP | 0.33251 | 0.3508 | 0.33998 | 0.86665 | 0.893 | 0.92288 | 0.35754 | 0.31672 | 0.32557 | 0.34728 | 0.31332 | 0.3106 | 0.27074 | 0.24531 | 0.24972
DUP | 0.088734 | 0.075518 | 0.068501 | 0.34271 | 0.28754 | 0.18568 | 0.16738 | 0.15948 | 0.11374 | 0.13532 | 0.10655 | 0.090035 | 0.12303 | 0.11518 | 0.1175
PP | 0.19888 | 0.19111 | 0.19461 | 1.4752 | 0.97052 | 0.57716 | 0.8662 | 0.54824 | 0.3866 | 0.66059 | 0.42627 | 0.33094 | 0.39506 | 0.23473 | 0.17928

## Slide 36
Results
Laboratory-scale tests
Most effective amendments identified by the batch-scale tests
Pig slurry1 | Dairy cattle slurry2 | Dairy soiled water3
Alum | Alum | Alum
Poly-aluminium chloride | Poly-aluminium chloride | 
Ferric chloride (FeCl3) | Ferric chloride (FeCl3) | Ferric chloride (FeCl3)
Lime | Lime | Lime
 | Aluminium-based sludge | Bottom ash
 | Flue-gas desulfurization by-product (FGD) | 
1 O’ Flynn, C.J., Fenton, O., Wilson, P., Healy, M.G. (2012) J. Environ Manage 113: 78-84
2 Brennan, R.B., Fenton, O., Grant, J., Healy, M.G. (2011) Sci Tot Environ 409: 5111-5118
3 Serrenho, A., Fenton, O., Murphy, P., Grant, J. Healy, M.G. (2012) Sci Tot Env 430: 1-7.

## Slide 37
Results
Laboratory-scale tests
Pig slurry1 | Dairy cattle slurry2 | Dairy soiled water3
Alum | Alum | Alum
Poly-aluminium chloride | Poly-aluminium chloride | 
Ferric chloride (FeCl3) |  | Ferric chloride (FeCl3)
1 O’ Flynn, C.J., Fenton, O., Wilson, P., Healy, M.G. (2012) J. Environ Manage 113: 78-84
2 Brennan, R.B., Fenton, O., Grant, J., Healy, M.G. (2011) Sci Tot Environ 409: 5111-5118
3 Serrenho, A., Fenton, O., Murphy, P., Grant, J. Healy, M.G. (2012) Sci Tot Env 430: 1-7.

## Slide 38
Methodology
Identification of amendments
Determine how much amendments to use per unit volume of wastewater
Efficacy of amendments at laboratory-scale
Efficacy of amendments at field plot-scale
Efficacy of amendments at field-scale
Batch-scale tests
Laboratory-scale tests
Plot and field-scale tests

## Slide 39: Plot-scale study
Plot isolated using PVC sheeting (50 mm below soil surface)
Slurry applied at 33 m3 ha-1
Rainfall simulators used to apply rain 2, 10 and 28 days after slurry application date
Intensity 10.5 mm hr-1

## Slide 41
Brennan et al. 2012. Sci Tot Env 441: 132-140.
Phosphorus in runoff from dairy cattle slurry

## Slide 42
Results
Field plot-scale tests
Pig slurry | Dairy cattle slurry1 | Dairy soiled water
Alum | Alum | Alum
Poly-aluminium chloride | Poly-aluminium chloride | 
Ferric chloride (FeCl3) |  | Ferric chloride (FeCl2)
Lime |  | Lime
 |  | Bottom ash
1 Brennan, R., Healy, M.G., Grant, J., Ibrahim, T.G., Fenton, O. (2012) Sci Tot Env 441: 132-140

## Slide 43
Results
Field plot-scale tests
Pig slurry | Dairy cattle slurry1 | Dairy soiled water
Alum |  | Alum
Poly-aluminium chloride | Poly-aluminium chloride | 
Ferric chloride (FeCl3) |  | Ferric chloride (FeCl2)
Lime |  | Lime
 |  | Bottom ash
1 Brennan, R., Healy, M.G., Grant, J., Ibrahim, T.G., Fenton, O. (2012) Sci Tot Env 441: 132-140

## Slide 44
Results
Field plot-scale tests
Taking into account GHG emissions, subsurface leaching, long-term impact
Pig slurry | Dairy cattle slurry1 | Dairy soiled water
 |  | Alum
Poly-aluminium chloride | Poly-aluminium chloride | 

## Slide 45
Conclusions
Due to the high cost of amendments, their incorporation into existing management practices can only be justified on a targeted basis where inherent soil characteristics deem their usage suitable to receive amended slurry.
It is prudent for farmers to adhere, whenever possible, to the 48-h rule (SI 610 of 2010) to reduce the risk of surface runoff of nutrients and sediment.

## Slide 46
Acknowledgements