## Slide 1: Comparison of intermittently loaded laboratory filter systems to treat dairy soiled water
John Murnane, Mark Healy, Owen Fenton
Environ 2016

## Slide 2
Dairy Soiled Water (DSW)
(as defined in SI 31 of 2014)
Contaminated washwater from farmyards, milking parlours, silage effluent etc.
BOD5 < 2,500 mg L-1;
DM content < 1%
Agronomic issues:-
Increased cost of on farm storage;
Large volumes can be generated from open yard areas during periods of prolonged or high intensity rainfall.
Environmental issues:-
Historically spread to agricultural lands - previously no closed season;
Can result in runoff to surface waters, particularly high when land is saturated, leading to:-
  incidental (event specific) P, N and organic carbon in runoff;
  can contribute to eutrophication of surface waters – ecology;
  can contribute to carbon load in surface waters – may have health implications for downstream water abstraction (trihalomethane formation in presence of high TOC levels)
Issues associated with dairy soiled water

## Slide 3: Study Aim
Generally:-
to compare passive filtration methods to treat DSW;
Specifically:-
to examine the impact of media depth, media type and organic loading rates (OLR’s) on the treatment of DSW by filtration.
Laboratory based study using on-farm DSW which will inform operation of field based unit.

## Slide 4: Materials and Methods
Farm generated DSW intermittently loaded onto columns in temperature controlled room
Intermittently loaded aerobic columns
Comparisons:-
Media depth (woodchip 600 mm v 1000 mm) – 100 days, avg. OLR = 120 g COD/m2/d.
600 mm deep woodchip v 1000 mm deep woodchip

## Slide 5: Materials and Methods
Farm generated DSW intermittently loaded onto columns in temperature controlled room
Treated effluent collection
Comparisons:-
OLR (1000 mm woodchip media) – 100 days; 52 v 127 g COD/m2/d.
52 g COD/m2/d v 127 g COD/m2/d

## Slide 6: Materials and Methods
Farm generated DSW intermittently loaded onto columns in temperature controlled room
Hydraulic tests being carried out on columns
Comparisons:-
Media type (woodchip v sand) – 212 days, avg. OLR = 35 g COD/m2/d
1000 mm woodchip v 1000 mm sand

## Slide 7: Materials and Methods
Laboratory analyses
Influent & effluent samples tested for:-
CODt, CODf, TOC, TIC;
SS, pH, DM;
TNt, TNf, NH4-N, NO2-N, NO3-N;
TP, TDP, PO4-P, DUP

## Slide 8: Key Results Impact of media depth (woodchip 600 mm v 1000 mm; average OLR = 120 g COD/m2/d)
Chart: Time (d)
| 0
Avg. OLR = 112 g COD/m2/d | 0
Influent SS (600 mm) | 426.6667 | 587.7778 | 763.3333 | 810 | 623.3333 | 730 | 1190 | 1040 | 1390 | 366.6667 | 655 | 690
Effluent SS (600 mm) | 208.3333 | 276.6667 | 271.6667 | 286.6667 | 273.3333 | 293.3333 | 290 | 486.6667 | 706.6667 | 96.6667 | 621.6667 | 450
Influent SS (1000 mm) | 520 | 485.5556 | 656.6667 | 578.3333 | 968.3333 | 803.3333 | 335 | 666.6667 | 676.6667
Effluent SS (1000 mm) | 42.9167 | 22.3333 | 7.9167 | 35 | 68.3611 | 28.8889 | 71 | 15.4167 | 43.7778
Suspended solids
Higher average SS removals for deeper (1000 mm) woodchip media
SS↓54%
SS↓94%

## Slide 9: Key Results Impact of media depth (woodchip 600 mm v 1000 mm; average OLR = 120 g COD/m2/d)
Chart: Time (d)
| 0
Woodchip media, Avg OLR = 112 g COD/m2/d | 0
Influent NH4 (600 mm) | 39.2817 | 38.317 | 105.6687 | 102.6333 | 103.646 | 98.131 | 110.1457 | 53.0383 | 127.7557 | 44.27 | 39.0727 | 62.0973
Effluent NH4 (600 mm) | 52.0727 | 106.1377 | 107.7243 | 102.9653 | 121.856 | 104.897 | 105.7613 | 80.2867 | 108.4033 | 46.6043 | 23.8333 | 36.2927
Influent NH4 (1000 mm) | 86.4813 | 54.696 | 83.5977 | 73.576 | 61.8097 | 64.234 | 66.0897 | 45.315 | 43.812
Effluent NH4 (1000 mm) | 1.1617 | 10.5337 | 1.1657 | 0.212 | 8.1997 | 9.8953 | 6.346 | 1.0897 | 2.7487
Ammonium
Higher average NH4-N removals for deeper (1000 mm) woodchip media;
No nitrification - both depths
No reduction
NH4-N↓82%

## Slide 10: Key Results Impact of media depth (woodchip 600 mm v 1000 mm; average OLR = 120 g COD/m2/d)
Chart: Time (d)
| 0
Woodchip media, Avg OLR = 112 g COD/m2/d | 0
Influent PO4-P (600 mm) | 7.9917 | 9.409 | 21.184 | 24.246 | 27.6817 | 49.1057 | 41.928 | 30.007 | 21.6283 | 3.2763 | 8.17 | 12.0437
Effluent PO4-P (600 mm) | 9.2313 | 11.106 | 10.5823 | 20.5027 | 28.2753 | 48.8993 | 41.3143 | 30.6537 | 20.8737 | 10.2493 | 9.696 | 11.7183
Influent PO4-P (1000 mm) | 22.718 | 16.6887 | 37.139 | 29.484 | 32.595 | 30.74 | 9.1318 | 9.176 | 9.6987
Effluent PO4-P (1000 mm) | 12.6857 | 15.5647 | 13.1867 | 6.9993 | 9.118 | 7.539 | 8.2998 | 8.917 | 9.3347
Orthophosphate
Higher average PO4-P removals for deeper (1000 mm) woodchip media
No PO4-P reduction
PO4-P↓51%

## Slide 11: Key Results Impact of OLR (1000 mm woodchip media; average OLR’s = 52 v 127 g COD/m2/d)
Key contaminants
No significant difference between removal rates for the two different OLR’s
Parameter | OLR | Average influent | Average effluent | % reduction
 | g COC/m2/d | mg L-1 | mg L-1 | 
COD | 52 | 3,347 | 766 | 77
 | 127 | 3,458 | 606 | 82
TOC | 52 | 377 | 205 | 46
 | 127 | 364 | 199 | 45
NH4-N | 52 | 47 | 3 | 94
 | 127 | 64 | 5 | 93
PO4-P | 52 | 15 | 7 | 54
 | 127 | 21 | 10 | 51
SS | 52 | 1,348 | 23 | 98
 | 127 | 632 | 37 | 94

## Slide 12: Key Results Impact of media type (woodchip v sand; depth 1000 mm; average OLR = 35 g COD/m2/d)
Chart: Time (d)
| 0
Col 3 (1000 mm deep - Woodchip), Avg OLR = 33 g COD/m2/d | 0
Influent CODt (woodchip) | 404.3547 | 1194.942 | 1361.108 | 1278.058 | 2193.0387 | 1035.65 | 4576.7213 | 4980.466 | 4877.9227 | 2421.062 | 1443.752 | 1968.3713 | 4569.408 | 3202.8773 | 3347.612
Effluent CODt (woodchip) | 650.3533 | 988.134 | 1040.912 | 519.312 | 743.9027 | 943.06 | 747.7547 | 814.514 | 364.728 | 984.747 | 989.422 | 1181.2985 | 1106.466 | 1093.1397 | 1143.0973
Influent CODt (sand) | 4877.9227 | 2421.062 | 1443.752 | 1968.3713 | 4569.408 | 3202.8773 | 3347.612 | 3437.5067 | 3391.06 | 1148.6613 | 1697.848 | 1580.4053 | 2795.138 | 2400.532 | 1448.302 | 1516.008
Effluent CODt (sand) | 50.2908 | 157.5259 | 146.1562 | 82.5829 | 72.1767 | 140.5327 | 115.1606 | 117.6199 | 140.501 | 159.4911 | 180.0625 | 175.0015 | 204.687 | 251.4641 | 206.1457 | 133.7887
COD
Sand has higher COD removal (avg. 146 mg L-1)but woodchip also produces consistent effluent COD (avg. 887 mg L-1)
COD↓66%
COD↓94%

## Slide 13: Key Results Impact of media type (woodchip v sand; depth = 1000 mm; average OLR = 35 g COD/m2/d)
Chart: Time (d)
| 0
Col 3 (1000 mm deep - Woodchip), Avg OLR = 33 g COD/m2/d | 0
Influent NH4-N (woodchip) | 23 | 45.315 | #N/A | #N/A | 38.202 | 45.591 | 49.0353 | 64.065 | 36.824 | 46.3032 | 87.668 | 99.1563 | 103.332 | 75.5333 | 75.8067
Effluent NH4-N (woodchip) | 5.5 | 1.0897 | #N/A | #N/A | 0.45233 | 11.385 | 2.878 | 1.6653 | 0.14633 | 1.5312 | 1.004 | 0.96733 | 1.1557 | 0.61567 | 0.58167
Influent NH4-N (sand) | 36.824 | 46.3032 | 87.668 | 99.1563 | 103.332 | 75.5333 | 75.8067 | 86.4813 | 54.696 | 83.5977 | 73.576 | 61.8097 | 64.234 | 46.0897 | 45.315 | 43.812
Effluent NH4-N (sand) | 0.509 | 1.8523 | 1.3113 | 1.1247 | 1.506 | 0.69933 | 0.997 | 1.171 | 0 | 0.603 | 0.27033 | 0.74033 | 0.39533 | 0.58933 | 0.677 | 0
Effluent NO3-N (sand) | 9.093 | 48.1875 | 38.7657 | 45.364 | 55.7243 | 58.0323 | 9.418 | 8.185 | 6.2873 | 6.5433 | 6.5207 | 5.136 | 7.25 | 9.3793 | 5.15 | 8.1193
Ammonium
No difference in NH4-N removal between sand (97% removal) and woodchip (99% removal);
Nitrified effluent produced by sand filters – initially reasonably high (≈ 50 mg L-1) but then at suppressed levels (≈ 10 mg L-1).
NO3-N

## Slide 14: Key Results Impact of media type (woodchip v sand; 1000 mm; average OLR = 35 g COD/m2/d)
Chart: Time (d)
| 0
Col 3 (1000 mm deep - Woodchip), Avg OLR = 33 g COD/m2/d | 0
Influent PO4-P (woodchip) | 9.1318 | 9.176 | 9.6987 | #N/A | 16.774 | 15.281 | 12.453 | 11.4637 | 15.4217 | 16.4233 | 22.733 | 29.709 | 27.923 | 21.72 | 21.56
Effluent PO4-P (woodchip) | 8.2998 | 8.917 | 9.3347 | #N/A | 16.3497 | 15.4773 | 3.463 | 2.9437 | 1.9583 | 0.18644 | 1.7397 | 2.4767 | 4.9387 | 7.6543 | 10.533
Influent PO4-P (sand) | 15.4217 | 16.4233 | 22.733 | 29.709 | 27.923 | 21.72 | 21.56 | 22.718 | 16.6887 | 32.139 | 29.484 | 29.595 | 30.74 | 9.1318 | 9.176 | 9.6987
Effluent PO4-P (sand) | 0.026333 | 0 | 0.10133 | 0.086333 | 0.027333 | 0.0026667 | 0 | 0.367 | 0.057667 | 0.05 | 11.926 | 11.7993 | 10.235 | 10.0768 | 12.6037 | 9.7163
150 days | 0 | 15
Orthophosphate
Sand has better (complete) DRP removal compared to woodchip up to 150 days, thereafter no significant difference between the two (DRP leaching from both > 150 days).
DRP↓59%
(<150d)
DRP↓100%
(<150d)

## Slide 15: Summary of key findings
Depth ≥ 1000 mm required for woodchip media to ensure enhanced N, P and SS removals;
Woodchip media depths investigated did not differ significantly for COD/TOC removal;
Woodchip media did not nitrify the effluent at both depths (600 and 1000 mm);
OLR did not significantly impact contaminant removal efficiencies of woodchip filters – robust removals at avg. 52 and 127 g COD/m2/d;
Sand enhances removals of COD, NH4-N and PO4-P compared to woodchip at avg. OLR’s of 35 g COD/m2/d and media depths of 1000 mm;
P leaching from sand and woodchip at ≈ 150 days for avg. OLR of 35 g COD/m2/d and media depth of 1000 mm;
Sand media produces consistent but low nitrification levels (≈ 10 mg NO3-N L-1) at avg. OLR of 35 g COD/m2/d and media depth of 1000 mm.

## Slide 16: Implications for on-farm treatment
Taking woodchip as the more robust media:-
Avg. DSW produced per cow = 9,784 L yr-1
Assume treatment at avg. OLR ≈ 90 g COD/m2/d (avg. of 52/127)
Take avg. COD of DSW = 2,750 mg L-1
Filter area required for 100 cow unit = = 82
BUT
media needs to be replaced every 80 – 100 days to prevent P breakthrough (i.e. 3 – 4 times per year).
Observations:-
Removal of SS to prevent clogging of filter media is a very important consideration for operation of filters (need settlement tank prior to loading onto filter);
Filters will only work with good on-farm management – important not to let the solids build up and regular media replacement;
DSW strength varies significantly and seasonally – particularly strong in Spring when cows on grass for first time after being housed for the winter.